## Slide 1
Tools for the optimal operation
and planning of power systems
Lecture 1: Introduction to operations research
Álvaro García-Cerezo
Power and Energy Analysis and Research Laboratory
School of Industrial and Aerospace Engineering of Toledo, Spain
Universidad de Castilla-La Mancha, Spain

## Slide 2: Copyright
© 2026 Álvaro García Cerezo. This document is licensed under a Creative Commons Attribution 4.0 International License (CC BY 4.0).
https://creativecommons.org/licenses/by/4.0/

## Slide 3: Contents
Introduction
Classification of Optimization Models
Linear Programming
Mixed Integer-Linear Programming
Nonlinear Programming
Optimization Software
Dual variables
Reformulation Techniques

## Slide 4: 1. Introduction

## Slide 5: Introduction
Optimization

## Slide 6: Introduction
To make the best decision

## Slide 7: Optimization
What is the best option?

## Slide 8: Optimization
It depends

## Slide 9: Optimization
To make the best decision
for a given objective function and subject to the
constraints of the problem

## Slide 10: Optimization
Objective function:
Minimize the cost / maximize the profit.
Maximize the renewable production.
Minimize the losses of energy.

## Slide 11: Optimization
Constraints:
Power balance.
Budget.
Technical limits.
Environmental and political limits.

## Slide 12: General formulation
s.t.:

## Slide 13: General formulation
s.t.:
Objective function

## Slide 14: General formulation
s.t.:
Variables

## Slide 15: General formulation
s.t.:
Subject to

## Slide 16: General formulation
s.t.:
Equality constraints

## Slide 17: General formulation
s.t.:
Inequality constraints

## Slide 18: General formulation
s.t.:
s.t.:

## Slide 19: Applications to Power Systems
Participation in electricity markets.
Security of power systems.
Participation in demand response programs.
Investment in transmission lines, generating units, and storage facilities.

## Slide 20: What will you learn?
To classify optimization models.
To solve optimization problems graphically.
To solve optimization problems using computational tools.
To reformulate nonlinear optimization problems.
The meaning of dual variables.

## Slide 21: 2. Classification of Optimization Models

## Slide 22: Classification of optimization problems
What is mathematical optimization?
https://www.youtube.com/watch?v=AM6BY4btj-M

## Slide 23: Classification of optimization problems
Model Type | Abbreviation | Terms | Variables
Linear Programming | LP | Linear | Continuous
Mixed-Integer Linear Programming | MILP | Linear | Integer and continuous
Nonlinear Programming | NLP | Nonlinear and linear | Continuous

## Slide 24: Classification of optimization problems
There are other types, such as:
Model Type | Abbreviation | Terms | Variables
Mixed-Integer Nonlinear Programming | MINLP | Nonlinear and linear | Integer and continuous

## Slide 25: Classification of optimization problems
LP Easy to solve.
MILP It depends on the number of binary variables and the problem addressed.
NLP (Generally) Hard to solve.

## Slide 26: Classification of optimization problems
M. Carrión, R. Domínguez, and G. Oggioni, “Optimal participation of wind power producers in a hybrid intraday market: a multi-stage stochastic approach”, Energy Economics, vol. 144, art. no. 108303, Apr. 2025, DOI: 10.1016/j.eneco.2025.108303.
LP problem:
Continuous variables: 3.8 million.
Constraints: 3.7 million.
Computational time: lower than 1 min.

## Slide 27: Classification of optimization problems
Á. García-Cerezo, P. M. Drašković, and H. Pandžić, “Day-ahead market scheduling strategy of a virtual power plant under the single imbalance pricing scheme via stochastic robust optimization”, paper submitted to Energy Economics.
MILP problem:
Continuous variables: 14,337.
Integer variables: 1,008.
Constraints: 12,372.
Computational time: 3 min.

## Slide 28: Classification of optimization problems
Á. García-Cerezo, A. Pleite-Paniagua, L. Baringo, and R. Domínguez, “Uncertainty-driven long-term participation of a virtual power plant in the day-ahead market and a grid-balancing demand response auction”, 24th Conference of the International Federation of Operational Research Societies (IFORS 2026), Vienna, Austria, Jul. 2026.
MILP problem:
Continuous variables: 1,329,631.
Integer variables: 129,990.
Constraints: 2,436,066.
Computational time: 1 h.

## Slide 29: Classification of optimization problems
Á. García-Cerezo, R. García-Bertrand, and L. Baringo, “Computational performance enhancement strategies for risk-averse two-stage stochastic generation and transmission network expansion planning”, IEEE Transactions on Power Systems, vol. 39, no. 1, pp. 273–286, Jan. 2024, DOI: 10.1109/TPWRS.2023.3236397.
MILP problem:
Continuous variables: 1,544,135.
Integer variables: 272,017.
Constraints: 3,570,235.
Computational time: not solved after 168 h (1 week).

## Slide 30: Classification of optimization problems
J. Muñoz Pedrosa, “Planning and operational decision-making for an industrial plant with self-consumption”, Bachelor’s Final Project, Electrical Engineering Degree, Universidad de Castilla-La Mancha, supervised by Á. García-Cerezo and M. Cañas-Carretón, Jul. 2026.
MINLP problem: not solved after 24 h (1 day).

## Slide 31: Classification of optimization problems
Not all NLP and MINLP problems are hard to solve:
Model Type | Abbreviation | Terms | Variables
Mixed-Integer Quadratically Constrained Quadratic Programming | MIQCQP | Quadratic and linear | Integer and continuous

## Slide 32: Classification of optimization problems
J. Muñoz Pedrosa, “Planning and operational decision-making for an industrial plant with self-consumption”, Bachelor’s Final Project, Electrical Engineering Degree, Universidad de Castilla-La Mancha, supervised by Á. García-Cerezo and M. Cañas-Carretón, Jul. 2026.
MINLP problem: not solved after 24 h (1 day).
MIQCQP problem: 3 min.
The optimization problem was THE SAME.
We only changed how the optimization problem was modeled.

## Slide 33: Convexity
Convex problem
Nonconvex problem

## Slide 34: Convex function and set

## Slide 35: Nonconvex function and set

## Slide 36: Convexity
Convex set and convex function
https://www.youtube.com/watch?v=a_gRfwHUlhQ
Convexity and the principle of duality
https://www.youtube.com/watch?v=d0CF3d5aEGc

## Slide 37: Convexity
LP Convex
MILP Nonconvex
NLP Convex or Nonconvex
MINLP Nonconvex

## Slide 38: Convexity
Integer variables Nonconvex
BE CAREFULL
INCLUDING
INTEGER VARIABLES

## Slide 39: High computational times
Sometimes the optimization problems cannot be directly solved due to the high computational burden.
We can:
Use approximation techniques (lecture 3).
Use decomposition techniques (lecture 4).

## Slide 40: 3. Linear Programming (LP)

## Slide 41: Example 1
s.t.:

## Slide 42: Example 1
s.t.:
Objective function

## Slide 43: Example 1
s.t.:
Variables (output data)

## Slide 44: Example 1
s.t.:
Constraints

## Slide 45: Example 1
s.t.:
Parameters (input data)

## Slide 46: Example 1
s.t.:

## Slide 47: Example 1
s.t.:

## Slide 48: Example 1
s.t.:

## Slide 49: Example 1
s.t.:

## Slide 50: Example 1
s.t.:

## Slide 51: Example 1
s.t.:
Feasible region

## Slide 52: Example 1
Some possible solutions:
1) , .
2) , .

## Slide 53: Example 1
Some possible solutions of :
1) , .
2) , .
Objective function line associated with

## Slide 54: Example 1
Objective function value
Objective
function value

## Slide 55: Example 1
0

## Slide 56: Example 1
0
3

## Slide 57: Example 1
10
0
3

## Slide 58: Example 1
10
0
3
13

## Slide 59: Example 1
Optimal solution:

## Slide 60: Simplex Method
10
0
3
13

## Slide 61: Simplex Method
Channel of Prof. Yong Wang (Binghamton University):
Basic Feasible Solution:
https://www.youtube.com/watch?v=0P5OAcXdUec
Graphical Explanation:
https://www.youtube.com/watch?v=Mz__0uBb2-U

## Slide 62: Example 2
s.t.:

## Slide 63: Example 2
s.t.:
Optimal solution:

## Slide 64: Example 3
s.t.:

## Slide 65: Example 3
s.t.:

## Slide 66: Example 3
s.t.:
Unbounded problem

## Slide 67: Example 4
s.t.:

## Slide 68: Example 4
s.t.:

## Slide 69: Example 4
s.t.:
Infeasible problem

## Slide 70: Example 5
s.t.:

## Slide 71: Example 5
s.t.:

## Slide 72: Example 5
s.t.:

## Slide 73: Example 5
s.t.:
Optimal solution:

## Slide 74: Example 5
s.t.:
Inactive constraints (they do not influence the optimal solution)

## Slide 75: Example 5
Example 1: .
Example 5: .
In a maximization/minimization problem, adding constraints leads to an objective function value lower/greater than or equal to the objective function value obtained without the additional constraints.

## Slide 76: Example 6
s.t.:

## Slide 77: Example 6
s.t.:
Feasible region

## Slide 78: Example 6
s.t.:

## Slide 79: Example 6
Optimal solution:

## Slide 80: 4. Mixed-Integer Linear Programming (MILP)

## Slide 81: Example 7
s.t.:

## Slide 82: Example 7
s.t.:

## Slide 83: Example 7
s.t.:

## Slide 84: Example 7
s.t.:

## Slide 85: Example 7
Optimal solution:

## Slide 86: Example 8
s.t.:

## Slide 87: Example 8
s.t.:

## Slide 88: Example 8
s.t.:

## Slide 89: Example 8
Optimal solution:

## Slide 90: Branch and Bound
Algorithm based on the use of a relaxed formulation.
Integer variables Continuous variables.
Iterative procedure All the search tree is analyzed or the optimality GAP condition is fulfilled: if , continue; otherwise, stop.
A relative optimality GAP condition can also be considered: if , continue; otherwise, stop.

## Slide 91: Branch and Bound
If , we cannot claim that the solution found is the global optimum.
However, the solution may be good enough for the decision maker.
https://www.youtube.com/watch?v=tBUfL3O_Nzg

## Slide 92: 5. Nonlinear Programming (NLP)

## Slide 93: Example 9
s.t.:

## Slide 94: Example 9
s.t.:

## Slide 95: Example 9
Optimal solution:

## Slide 96: Example 10
s.t.:

## Slide 97: Example 10
s.t.:

## Slide 98: Example 10
Optimal solution:

## Slide 99: 6. Optimization Software

## Slide 100: Optimization Software
GAMS: General Algebraic Modeling System.
Pyomo.
AMPL.
AIMMS.
JuMP.
…

## Slide 101: GAMS
Get started:
https://www.gams.com/free-licenses/#get-started
Download:
https://www.gams.com/download/
Documentation:
https://www.gams.com/latest/docs/index.html

## Slide 102: Solvers
Gurobi.
IBM CPLEX
CONOPT.
MOSEK.
KNITRO.
…

## Slide 103: Exercise 1
s.t.:
Optimal solution:

## Slide 104: Exercise 2
s.t.:
Optimal solution:

## Slide 105: Exercise 3
s.t.:
Optimal solution:

## Slide 106: Exercise 4
s.t.:
Optimal solution:

## Slide 107: Exercise 5
s.t.:
, , ,
Optimal solution:

## Slide 108: Notation
I will use the following notation in the course:
Uppercase letters Parameters (input data).
Lowercase letters Variables (output data).

## Slide 109: Exercise 6 – Compact formulation
s.t.:
,
Optimal solution:

## Slide 110: Exercise 7 – Sensitivity analysis
Solve exercise 6 for the following values of parameter : 0, 3, 8, 12, and 21. Use the LOOP statement in GAMS.
Solution:
(INFEASIBLE) Check the solution report.

## Slide 111: 7. Dual variables

## Slide 112: Dual variables
s.t.:
Dual variables

## Slide 113: Dual variables
Channel of Prof. Michel Bierlaire (École Polytechnique Fédérale de Lausanne):
Duality: duality in linear optimization
https://www.youtube.com/watch?v=R3Z1fRXXxyg
Duality: Lagrangian and dual problem
https://www.youtube.com/watch?v=4OifjG2kIJQ

## Slide 114: Formulation
I will consider hourly time periods for the sake of simplicity.
Hence, power (MW) and energy (MWh) units are equivalent.
If this is not the case, the duration of the time periods should be included in the formulation.

## Slide 115: Day-ahead electricity market
Demand
Power (MW)
Price (€/MWh)

## Slide 116: Day-ahead electricity market
Supply
Power (MW)
Price (€/MWh)

## Slide 117: Day-ahead electricity market
Price (€/MWh)
Power (MW)

## Slide 118: Day-ahead electricity market

## Slide 119: Day-ahead electricity market
Price (€/MWh)
Power (MW)
Consumer Surplus

## Slide 120: Day-ahead electricity market
Price (€/MWh)
Power (MW)
Producer Surplus

## Slide 121: Day-ahead electricity market
Price (€/MWh)
Power (MW)
Social Welfare

## Slide 122: Day-ahead electricity market
Price (€/MWh)
Power (MW)

## Slide 123: Day-ahead electricity market
Price (€/MWh)
Power (MW)

## Slide 124: Day-ahead electricity market
Price (€/MWh)
Power (MW)
s.t.:
Demand Supply
Constraints of the bids and offers

## Slide 125: Day-ahead electricity market
Price (€/MWh)
Power (MW)
s.t.:
Demand Supply
Constraints of the bids and offers

## Slide 126: Exercise 8 – Day-ahead electricity market
Consumer 1
Bid 1: 240 MW, €25/MWh.
Bid 2: 180 MW, €23/MWh.
Consumer 2
Bid 1: 147 MW, €19/MWh.
Bid 2: 110 MW, €18/MWh.

## Slide 127: Exercise 8 – Day-ahead electricity market
Producer 1
Offer 1: 217 MW, €18/MWh.
Offer 2: 200 MW, €20/MWh.
Producer 2
Offer 1: 220 MW, €21/MWh.
Offer 2: 250 MW, €25/MWh.

## Slide 128: Exercise 8 – Day-ahead electricity market
Determine the optimal solution of the day-ahead electricity market.
Solution:
Social Welfare €2171.
420 MW.
€21/MWh.

## Slide 129: 8. Reformulation Techniques

## Slide 130: Reformulation techniques
This section presents some reformulation techniques that I have used during my previous works:
Slack variables.
Product of two binary variables.
Product of continuous and binary variables.
Absolute value.
Square root.

## Slide 131: Slack variables
s.t.:
Infeasible problem

## Slide 132: Slack variables
s.t.:
where is a large constant such that and
Optimal solution:

## Slide 133: Slack variables
The use of slack variables is useful for example in transmission network expansion planning problems.
If the candidate transmission lines are not sufficient to satisfy the demand, then the slack variables are different from 0. Hence, the optimization problem must be solved again considering additional candidate transmission lines to ensure the feasibility of the problem, i.e., satisfy the demand.

## Slide 134: Product of two binary variables – Case 1
s.t.:
Nonlinear term:

## Slide 135: Product of two binary variables – Case 1
s.t.:
Nonlinear term:
s.t.:

## Slide 136: Product of two binary variables – Case 1
 |  |  |  | Result
 |  |  |  | Result

## Slide 137: Product of two binary variables – Case 2
s.t.:
Nonlinear term:

## Slide 138: Product of two binary variables – Case 2
We cannot replace with and .
Try it if you do not believe me.

## Slide 139: Product of two binary variables – Case 2
s.t.:
Nonlinear term:
s.t.:

## Slide 140: Product of two binary variables – Case 2
Note that .

## Slide 141: Product of continuous and binary variables
s.t.:
Nonlinear term:

## Slide 142: Product of continuous and binary variables
Disjunctive linearization
&
Big M method

## Slide 143: Product of continuous and binary variables
s.t.:
Nonlinear term:
s.t.:
where is a large constant

## Slide 144: Product of continuous and binary variables
If :
Note that and , i.e., .
The value of must be selected such that is not more restrictive than .
Different ’s can be used for upper and lower limits.

## Slide 145: Product of continuous and binary variables
If :
As mentioned before:
The value of must be selected such that is not more restrictive than .
Different ’s can be used for upper and lower limits.

## Slide 146: Product of continuous and binary variables
If , then .
If , then .
This means that .

## Slide 147: Product of continuous and binary variables
Additional comments:
Very large values of may lead to computational issues.
Constraints associated with must be checked ex post Trial-and-error method.
The proper values of can be known in some cases (see next slide).

## Slide 148: Product of continuous and binary variables
s.t.:

## Slide 149: Product of two continuous variables
Nonlinear term: in the objective function, an equality constraint or an inequality constraint.
We can discretize one of the continuous variables.
This approach is an approximation, not an exact reformulation!

## Slide 150: Product of two continuous variables
For example, we can consider some discrete values of one of the continuous variables:
Then, . The nonlinear terms of binary and continuous variables can be linearized as explained before.

## Slide 151: Product of two continuous variables
We can also use a binary expansion linearization (approximation):

## Slide 152: Absolute value
s.t.:
Nonlinear term:

## Slide 153: Absolute value
s.t.:
Nonlinear term:
s.t.:

## Slide 154: Absolute value
If :
Can be Not possible
Can be OK
Then, if .

## Slide 155: Absolute value
If :
Can be Not possible
Can be OK
Then, if .

## Slide 156: Absolute value
If , then .
If , then .
This means that .

## Slide 157: Square root
s.t.:
Nonlinear term:
This is an NLP problem.

## Slide 158: Square root
s.t.:
Nonlinear term:
This is an NLP problem.
s.t.:
Nonlinear terms: , , and .
This is a QCQP problem.

## Slide 159: Square root
The constraint acts as in practice because is considered in the objective function (minimization problem). Hence, .
Moreover, constraint should be considered to prevent the solution .
Therefore, the solution is .

## Slide 160: Next lecture
Lecture 1: Introduction to operations research.
Lecture 2: Operation and planning problems.
Lecture 3: Operational variability.
Lecture 4: Uncertainty and risk.
Lecture 5: Further applications.

## Slide 161: References
A. J. Conejo, E. Castillo, R. Mínguez, and R. García-Bertrand, Decomposition Techniques in Mathematical Programming: Engineering and Science Applications. Springer-Verlag, Berlin, 2006. ISBN: 3-540-27685-8. DOI: 10.1007/3-540-27686-6.

## Slide 162: References
A. J. Conejo and L. Baringo, Power System Operations. Springer, Cham, Switzerland, 2018. ISBN: 978-3-319-69406-1. DOI: 10.1007/978-3-319-69407-8.

## Slide 163: References
A. DeJeans Jr., The MILP Optimization Handbook: An Introduction to Linear and Integer Programming for Practitioners. BITBROS, 2025. ISBN: 979-8296430359.

## Slide 164: References
A. DeJeans Jr., The Linearization Handbook for MILP Optimization: Modeling Tricks and Patterns for Practitioners. BITBROS, 2025. ISBN: 979-8293657544.

## Slide 165
Thank you very much for your attention!
Contact: Alvaro.GarciaCerezo@uclm.es
Álvaro García-Cerezo
Power and Energy Analysis and Research Laboratory
School of Industrial and Aerospace Engineering of Toledo, Spain
Universidad de Castilla-La Mancha, Spain